## Slide 1
2024/06/03 Kojima Hikaru

## Slide 2: Index

## Slide 3: Background
input
output
Reserver is a device that work as a neural network by physical phenomenon.
Reflecting and interfering input light in the photonic reserver made that it store the state of a short time ago.
It seems that photonic reserver can predict chaotic-signal
and real-time graphic processing.

## Slide 4: Background
Reserver’s output is sum-of-product.
Reserver’s learning is only learning of weight of sum-of-product.
So reserver’s learning cost is fewer than machine learning.
However, it is difficult for light to calculate sum-of-product.
⇒only this part, calculate in electronic circuits.

## Slide 5: Background
This is a proposing analog multiplying circuit.
It modified gilbert multiplier for expand output amplitude.

## Slide 6: Purpose
Photonic reserver output by light and multiplier’s input is voltage.
So, we need photo-diode. But the output amplitude is smaller than multiplier’s input.
⇒It is necessary to photonic-electronic translator and amplifier that have dimension of resister.
This name is TIA(Trans-Impedance Amplifier)

## Slide 7: Single stage TIA
Photo-diode is a device of current output and multiplier’s input is voltage, so TIA needs current input and voltage output.
That is a reason why common-base amplifier is used for TIA.
But this topology is trade-off between trance-impedance and bandwidth.

## Slide 8: Double Stage TIA
To avoid the tread-off, I examining double stage TIA.
This topology dividing gain between two stage, I attempt high trans-impedance and large bandwidth.

## Slide 9: Double Stage TIA
This is a first stage of frequency characteristic.
This cutoff frequency is 10 GHz ordered.

## Slide 10: Double Stage TIA
input
VCC
GND
This is a second stage of frequency characteristic.
This cutoff frequency is 10 GHz ordered.